## Slide 1
Bandgap Design Report

## Slide 2: Introduction
- One of the essential building blocks of many analog circuits is a voltage reference, which should exhibit little dependence on supply and process parameters and a well-defined dependence on temperature.
- Temperature dependence: -
1- Positive temperature coefficient (+ve TC): Proportional to absolute temperature (PTAT).
2- Negative temperature coefficient (-ve TC): Complementary to absolute temperature (CTAT).
3- Temperature independent (Zero-TC): ZTAT = PTAT + CTAT.
- If we achieve a temperature independent reference it will also be process independent.
- Applications: Voltage regulators, ADCs and DACs, Biasing of amplifiers, Common-mode (CM) level of fully-differential circuits, ...etc.

## Slide 3: Band-gap Reference
- A reference voltage is generated by adding two voltages that have temperature coefficients of opposite sign with suitable multiplication constants.
- For example, for two voltages v1 and v2 that vary in opposite directions with temperature, choose a1 and a2 such that: -
a1(dv1/dT) + a2(dv2/dT) = 0
obtaining a reference voltage, VREF = a1.v1 + a2.v2 with zero TC.
- We must now identify two voltages that have positive and negative TCs. Among various device parameters in semiconductor technologies, the characteristics of bipolar transistors have proven the most reproducible and well-defined quantities that can provide positive and negative TCs.

## Slide 4: CTAT Voltage
- The base-emitter voltage of bipolar transistors or, more generally, the forward voltage of a pn-junction diode exhibits a negative TC.
❑ It can be shown that Vbe = const. − b1 T → CTAT
▪ Is is a strong function of temperature.
▪ b1 from simulations: Usually b1 ≈ 1.5 − 2 mV/K.

## Slide 5: PTAT Voltage
- If two bipolar transistors operate at unequal current densities, then the difference between their base-emitter voltages is directly proportional to the absolute temperature.

## Slide 6: Basic Band-gap Reference
- Adding a PTAT and CTAT in one circuit will produce a ZTAT voltage reference as shown in figure:
- The A-block is a circuit that makes V1 = V2 .
- The current mirror copies I2 to I1 and I3 .

## Slide 7: The PTAT Component

## Slide 8: The CTAT Component

## Slide 9: The ZTAT Reference Voltage

## Slide 10: The number of BJT's used

## Slide 11: Band-gap Reference Topologies 1- Current mirror based

## Slide 12: Band-gap Reference Topologies 2- Op-amp based

## Slide 13: The start-up Problem
- In the circuit of bandgap, if all of the transistors carry zero current when the supply is turned on, they may remain off indefinitely because the loop can support a zero current in both branches. So it is needed to inject current in the bandgap core for proper operation of the circuit. Start-up circuit does this job. This circuit also turns off when steady state is reached.

## Slide 14: Operation of start-up circuit

## Slide 15: Band-gap Curvature

## Slide 16: Proposed Band-gap Design

## Slide 17: Proposed Band-gap Design 1- Band-gap core

## Slide 18: Proposed Band-gap Design 1- Band-gap core
- VR2 = I2 × R2
= ((VBE2 − VBE1) / R3 ) x R2
= VT ln(n) × (R2 / R3)
= VT ln(8) × (R2/R3)
Where: [n = 8 for our circuit] and VT=KT/q.
- VR2 is a positive TC which is 1.94 mV/°C for the BJT’s used in this circuit.
- Vout =Vref= VR2 + VBE2, thus output voltage is actually summation of a positive TC and
a negative TC voltage. By choosing the proper value of resistors, output reference voltage is
made constant with respect to temperatures (Zero TC).

## Slide 19: Proposed Band-gap Design 2- Start-up Circuit

## Slide 20: Proposed Band-gap Design 2- Start-up Circuit
- At first Vref = 0 but M9 will be ON so there is current will flow in M9 and also in M10 so M11 will turn ON and it will pull down the voltage at current mirror gate down from Vdd and v+ of the op-amp will increase (so Vref no longer be zero) and when it reaches a value close to vdd then M11,M10,M9 will be OFF and at this moment the role of start-up circuit will be ended.

## Slide 21: Proposed Band-gap Design 3- Op-amp

## Slide 22: Proposed Band-gap Design 3- Op-amp
- Ideally our operational amplifier should have infinite gain for proper function of bandgap core. So for proper function of bandgap core we need to increase the gain of the circuit. That’s why a two stage operational amplifier has been used.
- But in a two stage amplifier, there is more than one pole which tries to make the circuit unstable. To make sure that the circuit is stable, stability analysis of the op amp has to be done.
- Another important aspect of OPAMP design is to produce a current which is insensitive to variation of VDD (supply voltage), this is accomplished by driving the operational amplifier with its own output current(self-biased), this makes the output current of operational amplifier almost constant with respect to voltage.

## Slide 23: Proposed Band-gap Design Complete circuit

## Slide 24: Analysis of Bandgap core
Vref = a1 VR2 + a2 VBE = const. => dVref/dT = a1 dVR2/dT + a2 dVBE/dT = 0
So a1(85uv/k) - a2(1.6mv/k) = 0
Since CTAT slope is greater than PTAT slope we will make a2=1 and vary a1 to make PTAT slope increasing to reach CTAT slope:
So a1=1.6m/85u => a1=19 = (R2/R1)*ln(8)
Let I=30uA then R1=VTln(8)/I = 2k ohm and R2= a1R1/ln(8) = 18k

## Slide 25: Analysis of the Op-amp

## Slide 26: Simulation of Bandgap 1- DC sweep vs Temperature
- Vdd = 3.3v and the temperature was swept from –40 to 120 c

## Slide 27: Simulation of Bandgap 2- DC sweep vs Supply voltage
- VDD was swept from 0 to 5v

## Slide 28: Simulation of Bandgap 2- Transient Analysis
- A step voltage from 0 to 5v volt used with 100 us rise time

## Slide 29: SPICE Netlist

## Slide 30: References
1- https://www.youtube.com/watch?v=wJz6claEGa0list=PLK2eyR1C9gjp5tk5j7eTYU_Th4IL_H83T
2- https://www.researchgate.net/publication/275341924_Design_of_a_Simple_CMOS_Bandgap_Reference
3- https://drive.google.com/drive/folders/1OWcbg8f48_ilr8jptdFEA3nbNeQyD0Hi